## Slide 1: Fiber Nonlinearity and Modeling
Optical Communications Networks
Spring 2021

## Slide 2: Physical topology of optical networks

## Slide 3: Optical fiber
An electromagnetic propagation media
First manufactured of copper, then silica
Imposing impairments on transmitted signal

## Slide 4: NLSE, a full description of optical fiber
Attenuation
Signal power loss
Dispersion (GVD)
Caused by dependence of fiber refractive index to frequency
Signal temporal spreading
Non-linear effect
Caused by dependence of fiber refractive index to power
Signal spectrum spreading
Propagating signal

## Slide 5: Duality between dispersion and non-linear effect
Dispersion
  Interaction between different times
  Phase rotation in frequency
  Easy to analyze! 
Non-linear effect
  Interaction between different frequencies
  Phase rotation in time
  Hard to analyze! 
Phase rotation due to the non-linear effect is called SPM. We also have other non-linear terms. More on this later…

## Slide 6: Amplified spontaneous emission
Excitation of electrons due to photon absorption
Originated at active elements
Mostly modeled as a Gaussian phenomena
Linear impact on signal

## Slide 7: SNR and optical reach
Example of behavior SNR versus power after
a fiber-optic link
Example of optimum power versus distance at fixed SNR

## Slide 8: Other contributions to NLSE
Accounting for dual-polarized propagation
Fiber birefringence
  Polarization variation through fiber
  Typically fast in space (~meters)
  Periodic over a beat length
  Matrix-form attenuation and dispersion

## Slide 9: Fiber propagation: numerical methods
Split-step Fourier method (SSFM)

## Slide 10: Non-linear phase rotation

## Slide 11: Fiber propagation: analytical perturbation modeling
Negligible non-linear perturbation around a large-scale signal
No major deviation from working point
Based on Taylor’s expansion
Fair to high accuracy for strongly dispersive fiber-optic systems
Accounting only for 1st-order non-linear effects
Enter the XPM and FWM!

## Slide 12: Fiber propagation: analytical perturbation modeling (cont’d)
Optical Fiber
<< Solving Manakov equation >>

## Slide 13: Dispersion compensated vs. uncompensated likns
Dispersion-compensated links
  Performed at the end of each link or span
  Fiber-grating dispersion-compensating module (FBG-DCM)
  Minimal to no compensation at receiver
Dispersion-uncompensated links
  Performed at the coherent transceivers
  Feasible thanks to DSP
  Capable of more non-linear mitigation due to time-domain signal spreading
  A suitable framework for non-linear models derivations

## Slide 14: Non-linear models for fiber propagation: the GN model
Optical Fiber
Optical Fiber
Input Signal
Input Signal
NLI Gaussian Noise
ASE Gaussian Noise
ASE Gaussian Noise
Output Signal
Output Signal

## Slide 15: Non-linear models for fiber propagation: roadmap
Perturbation Approach
Derivation Details

## Slide 16: GN model: discrete to continuous

## Slide 17: Applying GN model to multiple spans (incoherent)
Spans may have different spectrums!
The NLI noise is accumulated incoherently.
Dispersion is not compensated before the receiver.
Linear
Linear
+
Linear
+
NLI
NLI
NLI

## Slide 18: Corrections to GN model: the EGN model
The GN model is fairly accurate when,
  the symbol rate is large,
  fiber dispersion is large,
  loss per span is not too small,
  amplification is prevalently lumped and
  the number of traversed spans is sufficiently large.
This model overestimates NLI. Enhanced GN (EGN) model is a way out…
GN model is modulation independent, while EGN model is not.
Better analysis can be performed on new NLI terms SCI, XCI and MCI (in addition to SPM, XPM and FWM)

## Slide 19: NLI terms: SCI, XCI and MCI

## Slide 20: GN and EGN models accuracy comparison

## Slide 21: Employing models for PLI-aware optimization
Routing, modulation and spectrum assignment (RMSA)
  Allocation of available network resources (such as spans spectrums, modulation format and power) to demands
  First model applications including locally-optimal globally-optimal Nyquist (LOGON) strategy
  Traditionally investigated in full-load scenario (where links spectrums are fully occupied)
  Over-simplification by decoupling traffic pattern from NLI
  Making lightpaths insensitive to new connections
  Too pessimistic and sub-optimal!
LOGON strategy

## Slide 22: Employing Models for PLI-Aware Optimization (cont’d)
A 2nd application in RMSA
  Using stochastic processing
  Bounded probability of incorrectness
A 3rd application in RMSA
  Using models for machine-learning-based approaches
  Training a neural network based on positive and negative examples of feasible lightpaths

## Slide 23: Outlook toward the future of physical-layer models
More efficient non-linear mitigation through more complicated affordable DSP operations
Model simplification for optimization problems (in both static and dynamic cases)
Model generalization and development to novel applications (such as multi-mode fibers or higher-dimension modulation formats)
Accurate investigation of ASE and NLI interaction (important in low-SNR regime)