## Slide 1: Optical Protection
Chapters 7: J. M. Simmons,
Optical Network Design and Planning, Optical Networks,
© Springer International Publishing 2014

## Slide 2: Introduction
Failures are due to
fiber cuts, equipment failures, software errors,
technician errors, environmental causes, or
malicious attacks.
The optical protection mechanisms differ in the amount of spare capacity and equipment required, the speed of recovery, the number of concurrent failures from which recovery is possible, and the operational complexity.

## Slide 3: Protection and Restoration in Internet, cont’d
The most likely failures are single failures rather than double failures.
Multiple failures may also be considered, but with proper design, the
probability of having multiple failures can be made very small.
A physical failure will lead to one or more links failing at the client layers.
Single-component failures, for example, transceiver failure, can lead to
single-link failures.
A fiber cut can lead to multiple link failures at the client layer if fibers
carry multiple wavelengths.
Links that fail together due to a single failure event are referred to as
shared risk link Groups (SRLGs).
Single switch or router failures also lead to SRLGs since all links incident
to the switch or router will fail.

## Slide 4: Protection and Restoration in Internet, cont’d
Protection may be dedicated or shared.
In dedicated protection, each working connection is assigned its
own dedicated bandwidth in the network over which it can be
rerouted in case of a failure.
In shared protection, we make use of the fact that not all working
connections in the network fail simultaneously (for example, if they
are in different parts of the network).
An advantage of shared protection is that the protection bandwidth
is available to carry low-priority traffic under normal conditions.
This low-priority traffic is discarded in the event of a failure when
the bandwidth is needed to protect a connection.

## Slide 5: Protection and Restoration in Internet, cont’d
Protection schemes can either be revertive or nonrevertive.
In both schemes, if a failure occurs, traffic is switched from the working
path to the protect path.
In a nonrevertive scheme, the traffic remains on the protect path until
it is manually switched back onto the original working path, usually by
a user through the network management system.
In a revertive scheme, once the working path is repaired, the traffic is
automatically switched back from the protect path onto the working
path.
Dedicated protection schemes may be revertive or nonrevertive;
however, shared protection schemes are usually revertive.

## Slide 6: Dedicated Versus Shared Protection
One of the basic dichotomies among protection schemes is whether the protection is dedicated or shared
Dedicated Protection
  1+1 dedicated protection
  1:1 dedicated protection
      non-revertive mode
      revertive mode
Shared Protection

## Slide 9: 1+1 Protection
The 1+1 protected traffic is sent over two parallel paths,
and the destination selects a better one.
In case of failure, the destination switch onto the
other path.
Pros: simple for implementation and fast restoration
Cons: waste of bandwidth

## Slide 10: 1:1 Protection
During normal operation, no traffic or low priority traffic is
sent across the backup path.
In case failure both the source and destination switch onto
the protection path.
Pros: better network utilization.
Cons: required signaling overhead, slower restoration.

## Slide 11: Protection in Ring Network
1+1 Path Protection
Used in access rings for traffic aggregation into central office
1:1 Link Protection
Used for inter-office
rings
1:1 Span and Link Protection
Used in metropolitan or
long-haul rings
Unidirectional Path Switched Ring
Bidirectional Link Switched Ring
Bidirectional Link Switched Ring

## Slide 12: Unidirectional Path Switched Ring (UPSR)
Signal sent on both working
and protected path
Best quality signal selected
Receiving Traffic
N1 send data to N2
N1
N2
Outside Ring = Working
Inside Ring = Protection
Sending Traffic
N4
N3

## Slide 13: Bidirectional Link Switched Ring (2-Fiber BLSRs)
Sending/Receiving
Traffic
Sending/Receiving
Traffic
Both Rings = Working & Protection
N1
N2
N4
N3

## Slide 14: Protection in Mesh Networks
Working Path
Backup Path
Network planning and survivability design
  Disjoint path idea: service working route and its backup
  route are topologically diverse

## Slide 15: Path Protection / Link Protection
Path Switching: restoration is handled
by the source and the destination.
Normal Operation
Link Switching: restoration is handled
by the nodes adjacent to the failure.
Span Protection: if additional fiber is
available.

## Slide 16: Path Protection
Dedicated Path Protection
Shared Path Protection
Backup resources are used for protection of multiple links
The capacity reserved for protection is greatly reduced in the shared protection

## Slide 17: Reactive / Proactive
Reactive
  A search is initiated to find a
  new lightpath which does not
  use the failed components
  after the failure happens.
  It can not guarantee
  successful recovery,
  Longer restoration time
Proactive
  Backup lightpaths are
  identified and resources are
  reserved at the time of
  establishing the primary
  lightpath itself.
  100 percent restoration
  Faster recovery
Taxonomy

## Slide 18: Client-Side Versus Network-Side Protection

## Slide 19: Protection type
Transponder Protection
Wavelength Assignment with Network-Side Protection
1:N

## Slide 20: Ring Protection Versus Mesh Protection
Ring Protection
Network-side shared ring protection
Details of Node A

## Slide 21
Shared optical ring protection after Link EF fails
Optical Multiplex Section Shared Protection Ring (OMS-SPRing) protection
E-F-A-B E-F-E-D-C-B-A-B

## Slide 22: Mesh Protection

## Slide 23: Fault-Dependent Versus Fault-Independent Protection
In fault-dependent schemes, the protection used depends on where the failure has occurred
In fault-independent schemes, the same protection mechanism is used regardless of the fault location
Link Protection
Path Protection
Segment Protection

## Slide 24: Link Protection

## Slide 25: Path Protection
At the other extreme is fault-independent path protection.

## Slide 26: Segment Protection

## Slide 27: Multiple Concurrent Failures
Multiple Concurrent Failures: Without Catastrophes
  The most common cause of a link failure is a fiber cut or an amplifier failure
Multiple Concurrent Failures: With Catastrophes
  Catastrophes can be modeled as correlated link failures

## Slide 28: Protection Schemes for Multiple Concurrent Failures
1 + 2 Dedicated Protection
1 + 1(+ 1) Protection
1 + 1 + Shared Protection
Shared Protection
  working paths : dotted lines
  shared protection : dashed lines

## Slide 29: Protection through Dynamic Networking
If the second failure is on Link CD, then path A-C-F-G-E-Z is established for recovery

## Slide 30: Effect of Optical Amplifier Transients on Protection

## Slide 31: Shared Protection Based on Pre-deployed Subconnections
a= Shared protection based on pre-deployed
subconnections
b= Details of Node A
c= Details of Node H

## Slide 32: Cost Versus Spare Capacity Trade-off
a Three pre-deployed subconnections, requiring seven wavelength-links of capacity and six transponders.
b Four pre-deployed subconnections, requiring six wavelength-links of capacity and eight transponders

## Slide 33: Shared Protection Based on Pre-Cross-Connected Bandwidth
P-Cycles
If E-F breaks in A-F-E-D, new path is B-F-A-B-C-D-E-D.
Pre-cross-connected Trails

## Slide 34: Quiz
Consider a 3×6 grid network, where each link is 1,000 km in length and the optical reach is 3,000 km.
(a) Partition this network into the fewest number of transparent islands.
(More than one solution is possible.) Assume that all inter-island traffic is regenerated at a border node. Assuming one wavelength of bidirectional traffic between each pair of nodes, how many regenerations are required in your design?
(b) With the same traffic, what is the minimum number of regenerations required in a selective-regeneration architecture?