## Slide 1: Routing and Wavelength (Spectrum) Assignment
Optical Communications Networks
Spring 2021

## Slide 2: Routing and Wavelength (Spectrum) Assignment: Concepts
Allocating a route and wavelength (or spectrum slice) demands in a network
Effective use of both physical topology and traffic matrix
Considerations
  Cost
  Latency
  Availability
Having impacts on congestion and total carried traffic

## Slide 3: Terminology
Network nodes
  Sites that source, terminate and switch traffic
  Amplifier-only sites are NOT nodes!
Network links
  Optical fibers running between two nodes
  Almost always bidirectional with a separate fiber at each direction
  Also referred to as “hops”
Network topology
  Interconnection pattern of nodes
Nodal degree
  Number of incident fiber-pairs at node
Optical reach
  The distance that signal can traverse all-optically before requiring to be regenerated
  Specially important in backbone networks

## Slide 4: Terminology (cont’d)
Routing (R) and wavelength assignment (WA), together referred to as RWA
Regeneration
  Entering the WDM signal from optical to electrical domain and again, to optical
3R regeneration
  Re-amplification
  Re-shaping
  Re-timing
O-E-O architecture
  Signal regeneration at each intermediate node
  Large amount of equipment!
  Drawbacks in terms of cost, power consumption, reliability and space requirements
O-O-O (all-optical) architecture
  Signal being carried in optical domain throughout transmission
  Also referring to infrequent regeneration
  Reconfigurable optical add/drop multiplexers (ROADMs) for optical bypass

## Slide 5: O-E-O vs. O-O-O architecture
A recent research area:
Investigating regenerations also in a point on links not only nodes
In a typical network, shortest path was not the minimum-regeneration path for 1% of demands!

## Slide 6: Wavelength- vs. Spectrum Assignment
Wavelength
  Fixed griding
  Sub-optimal due to fixed-grid constraints
  Less contention-prone
  Simple design
Spectrum
  Flexible griding
  More optimal
  More contention-prone
  More complicated design

## Slide 7: RWA (RSA) Perspectives
WA (SA), O-O-O architecture
  Challenging design
  Wavelength continuity constraint
WA (SA), O-E-O architecture
  Simple problem of WA
Routing order
  Fulfilling more challenging demands first
Back-up paths for a connection
  Multiple candidates for a connection
Routing strategies
  Avoiding congestion
  Shortest path
  Minimum-hop
Wavelength contention
  Free capacity, but no free wavelength due to poor design!
  Heuristic algorithms
Joint routing and wavelength assignment
  More complicated algorithm as opposed to separate RWA
Impairment-aware RWA
  Exploiting models for capturing fiber impairments
Multicast routing

## Slide 8: RWA (RSA) Perspectives (cont’d)
Wavelength contention
  Free capacity, but no free wavelength due to poor design!
  Heuristic algorithms
Joint routing and wavelength assignment
  More complicated algorithm as opposed to separate RWA
Impairment-aware RWA
  Exploiting models for capturing fiber impairments

## Slide 9: Shortest-Path Routing Algorithms
Target
  Finding a path of minimum total metric (whether distance, hop, etc.)
Assumptions
  Additive cost
  No negative cycles in network
  (bidirectional links; indifference between source and destination)
Algorithms
  Dijkstra
    Minimum distance
    Greedy
    Always yielding a solution (if exists)
  Breadth-first-search (BFS)
    Minimum hop
    Link cost equal to 1
  Constrained shortest-path (CSP)
    Extra constraints on paths found (e.g. maximum number of hops not exceeding a threshold)

## Slide 10: k-Shortest-Paths Routing Algorithms
Target
  Generating a set of paths between source and destination
  Path distances in ascending order from the shortest up to k-th shortest
Benefits
  Better load balancing
  Avoiding congestion
Paths may have common links!

## Slide 11: Shortest-Distance Versus Minimum-Hop Routing
O-E-O architecture
  Cost equivalent to number of regenerations
  Setting link metric equal to 1
  Minimum-hop
O-O-O architecture
  Not a straightforward choice of metric 
  Running k-shortest-path algorithms twice (once with minimum-distance metric and again with unity metric) and finding the best path with minimum regeneration

## Slide 12: Protection Considerations in Routing
Service-level agreement (SLA)
  A formal contract between service costumer and service provider
  Availability
  Protection level against network failures
Disjoint-path routing for protection
Failure-dependent protection
  Restoration of a service path around a detected failure location
  Time-consuming!
Failure-independent protection
  Setting up backup paths prior to possible failures
  Typically link-disjoint
  Also node-disjoint for important services

## Slide 13: Methods for Finding Disjoint Paths
Method 1
  Running a shortest-path algorithm and finding an optimal path
  Removing the links of the path from network (topology pruning)
  Running the shortest-path algorithm again and finding another optimal path
  Returning the two results as final response
Method 2
  Using an original (!) shortest pair of disjoint paths (SPDPs) algorithm
  Minimal sum of link metrics over the resulting paths
  More advanced topology pruning
  Bhandari algorithm
    Also applicable to finding more than two desired paths
  Suurballe algorithm

## Slide 14: Drawbacks of Method 1
Suboptimal
Infeasible, trap topology

## Slide 15: Method 2: Bhandari Algorithm

## Slide 16: Method 2: Suurballe Algorithm
Link metric update:

## Slide 17: Scenarios with SPDP Algorithm Failure
Maximally disjoint paths

## Slide 18: Disjoint-Path Routing with Multiple Sources and/or Destinations

## Slide 19: Shared-Risk Link Group (SRLG)

## Slide 20: Routing Strategies
Fixed-path routing
  Same path for all connection requests between source and destination
  Blocking of new connections if links are congested
  Simple
  Non-adaptive
  Optimal from latency point of view
Alternative-path routing
  Many candidate paths for all connection requests between source and destination
  Choosing path for connection requests based on current network load
  Adaptive
  More time-consuming

## Slide 21: Routing Strategies (cont’d)
Dynamic routing
  No route pre-calculations, connection requests are processed once arrived!
  Dynamic change of link metrics
  Considerations
    Cost
    Load
  Most opportunity for adaptation to current network state
Pure dynamicity may be sub-optimal from the viewpoint of efficiently packing the wavebands.
Decision delay is a problem, specially in presence of a path-computation element (PCE).

## Slide 22: Routing Order
Ordering priority
  Whether or not a service requires protection
  Whether or not a service must be routed over hot links
  Service requested rate
  Distance between endpoints
Ordering algorithm (stimulated annealing)
  Finding a base result
  Swapping two services’ priorities
  Running the routing process again
  Checking the result from optimality point of view
  Update the result with a probability
  Proceed these steps long enough

## Slide 23: Multicast Routing
Multicast versus multiple unicasts
Saving capacity by a factor of 2 or 3

## Slide 24: Multicast Routing
Usage
  Media distribution
Multicast tree (Steiner tree)
  Tree cost as the sum of its link metrics
  Difficult problem of finding a minimum-cost Steiner tree
  Heuristics with good, approximate solutions
    Minimum-spanning tree with enhancement (MSTE)
    Minimum-paths (MP)
Multicast protection
  Large protection facilities!
  Protection of tree segments
  Network coding
    Reception of a linear combination of signals rather at each destination
Manycast routing
  Reaching N out of M destinations
  Usage
    Distributed computing
  A variation of MP algorithm to obtain the optimum tree

## Slide 25: Multicast Protection with respect to Regeneration Sites

## Slide 26: Wavelength Assignment
Allocating spectrum portions to routed connections
Also abbreviated to as WA
Cooperation with regeneration
  Wavelength conversion
  Back-2-back transponders

## Slide 27: Wavelength Assignment; Challenges
Major challenges
  Wavelength continuity in an optical segment of transmission
  Link utilization
There is a trade-off between WA simplicity and cost in presence of regeneration!

## Slide 28: Wavelength Assignment Failure
Four possible options
  Blocking the service (!)
  Changing the places of regeneration
  Changing the route
  Increasing the number of regenerations without re-routing
    Greater cost

## Slide 29: WA Studies; Figures of Merit
Sparse, but sufficient regeneration
  Regenerations due to optical reach constraints in backbone networks are mostly enough!
  In metro-core networks, regeneration may be offered by electrical-domain grooming.
Wavelength contention is a major cause of connection blocking.

## Slide 30: Wavelength Assignment Algorithms
WA problem as graph-coloring problem
Generating a conflict graph with lightpaths as nodes and their conflicts as links
Ordering the conflict graph nodes for coloring
  Well-researched topic
  Methods
    First-fit
    Most-used

## Slide 31: Wavelength Assignment Algorithms
First-fit
  Labelling and ordering available wavelengths from 1 to W
  Moving over lightpaths, assigning the least-indexed available wavelength for each lightpath
  No relation between wavelength indexing and wavelength position on spectrum!
    Manipulations can be made in purpose to satisfy some target.
Most-used
  Giving adaptive indices to wavelengths based on their current usage in network
  Indexing wavelengths from most-used to least-used from lowest to highest
  More computation
So, what is the motivation behind most-used?

## Slide 32: RWA Schemes
One-step RWA
  Solving the problems of routing and wavelength assignment together
  Better results
  Better in heavily-loaded networks
  More complicated!
Topology pruning
  Moving over wavelengths and reducing the network topology to those links with free capacity on that wavelength
Reachability graph transformation
  Breaking network topology to all-optical segments

## Slide 33: One-Step RWA; Reachability Graph Transformation
(Optical reach is 2,000km)

## Slide 34: RWA Schemes (cont’d)
Flow-Based Methods
  Modelling the RWA problem as ILP
  Very close to optimal
  Time-consuming
  Using LP with solution-rounding techniques
  Starting with candidates paths instead of a free-running of ILP
  Cost functions offering load-balancing
  Suitable for highly-loaded networks with low number of free wavelengths
ILP-Based Ring RWA
  Same as ILP-based RWA, though in ring topologies
  Dramatically faster due to ring structure
  Scalable
Further research suggestion:
Studying ILP-Based Ring RWA in mesh networks through decomposition

## Slide 35: Impairment-Aware Routing and Wavelength Assignment
RWA + physical-layer models
  Adaptive link metrics
  Effect of wavelength assignment on SPM, XPM and FWM
  Pseudo-linear regime as the most popular assumption
Strategy 1
  Worst-case
    Links fully loaded
    Guaranteed feasibility of later-added connections
    Leading to extra regenerations
    Too pessimistic!
Strategy 2
  Precise calculation of impairments on time
  Less regeneration
  Changeable condition of old services due to the new ones

## Slide 36: Worst-Case vs. Precise Impairment Calculation
When using precise calculation with no regeneration:
Reduction in blocking probability by an order of magnitude
Optical reach and precise calculation, are of less importance in metro networks.

## Slide 37: Impact of Impairments on RWA
Changing the link metrics based on their spectrum
  Using a modified Dijkstra algorithm to find may paths between source and destination
  Choosing a path out of many using a scalar function
Machine learning
  Estimating quality of transmission (QoT) for new connections
  Establishing databases before
  Indexing the stored paths in database based on their character
  Detecting resemblance of a new connection to paths in database and using those information in RWA

## Slide 38: Mixed Line-Rate Systems
Combination of line-rates of different amounts
  Carrying 10Gbps and 40Gbps signals together
  Detrimental effect of 10Gbps signals on 40Gbps signals due to XPM
Reasonable use of precise calculation of impairments due to escaping pessimistic design of worst-case strategy

## Slide 39: Elastic Optical Networks (EONs)
Arbitrary wavelength griding
Replacing grooming with spectrum-sliced elastic (SLICE) optical path architecture
  Allocating a flexible-bandwidth wavelength to a client service
  More power and cost efficient compared to grooming
  EONs are networks supporting SLICE

## Slide 40: EONs (cont’d)
OFDM
  Carrying a signal over multiple carriers
  More tolerable to fiber impairments
Software-controlled bandwidth-variable transponders (BVTs)
  Handling variable-rate
  Serving as multiple virtual transponders for narrow-bandwidth connections
Variable-bandwidth switches
  LCoS-WSSs
The limitation of filtering technology imposes the griding not to be totally unquantized. Rather, it must provide multiples of a base bandwidth called slot.

## Slide 41: EONs (cont’d)
Ideal and aggressively pursued for future network architecture

## Slide 42: RSA in EONs
Routing is the same!
Spectrum assignment
  Assigning a particular set of slots to an optical channel
  Continuity constraint
    Same slots must be assigned in an all-optical segment of transmission
    Similar to continuity in fixed-grid networks
  Contiguity constraint
    Slots must be assigned consecutively to a connection
    New concept in EONs!
More challenging and complicated design
Multi-step RSA is more reasonable.
The alternative-path routing is favored once again.
Both link-load and fragmentation are important now.

## Slide 43: RSA in EONs (cont’d)
Spectrum assignment
  Weighted graph-coloring
    More weights to connection requests with more required slots
  Considering contiguity
  Variations to first-fit and most-used
    First-last-fit
    Best-fit
    Exact-fit (reverting to first-fit)

## Slide 44: RSA in EONs (cont’d)
ILP-based RSA
  Constraints
    Unique spectrum assignment on a single fiber
    Continuity
    Contiguity
  Objective function
    Minimizing the maximum number of utilized slots on all links
    Minimizing the highest-numbered slot utilized on any link
    Minimizing the total number of slots utilized across the network
    Minimizing the amount of requested bandwidth that is blocked
Distance-adaptive RSA
  Routing, modulation level and spectrum assignment (RMLSA)
  Including modulation level for transmission reach maximization
  Transmission degradation due to multiple modulation formats in fibers
Routing, Spectrum and Core Assignment (RSCA)
  Including multi-core fibers and space-division multiplexing
  Crosstalk between cores 

## Slide 45: Defragmentation
Saving stranded bandwidth and displacing gaps

## Slide 46: Push-Pull Defragmentation

## Slide 47
Any Questions?