## Slide 1: An Introduction to SSFM and EGN Simulations
Mostafa Ayaz
Optical Networks
March 2021

## Slide 2: What is SSFM?
A recursive way for solving the dual-polarized Manakov’s equation
Transmitter, receiver and optical transmission media simulation
Taking advantage of Fourier synthesis and analysis transforms periodically
Highly accurate!
Capable of handling all scenarios (no limits)
Highly time-consuming as well!
Unsuitable for modeling, specially when studying parameter effects on transmission

## Slide 3: SSFM in a General Schema
WDM signal construction at transmitter
Signal propagation through nodes and links
Signal reception and data detection process
SNR (and possibly SER) calculation from TX and RX data
Transmitter
Receiver
Optical Media

## Slide 4: WDM Transmitter
MUX
Symbol Sequence Generation
Carrier Modulation
Pulse Shaping
Symbol Sequence Generation
Carrier Modulation
Pulse Shaping
Symbol Sequence Generation
Carrier Modulation
Pulse Shaping
.
.
.
User 1
User N
User 2
freq_D
time_D
TX out
Used for discrete filtering

## Slide 5: WDM Signal Spectrum
Continuous frequency domain of WDM signal
Discrete frequency domain of WDM signal

## Slide 6: Optical Transmission Media
Optical Fiber
G
Optical Fiber
G
Optical Fiber
G
LIN
LIN
Too many fiber sections!
NL
Many spans!
Point-to-Point (P2P) Transmission [Single Link]

## Slide 7: Pseudo-Code for Link Transmission Simulation
for span in spans_of_link do:
  for fiber_section in span_fiber_sections do:
    Apply the half linear effects on frequency-domain signal
    Calculate the time-domain of signal
    Apply the non-linear span effects on time-domain signal
    Calculate the frequency-domain of signal
    Apply the half linear effects on frequency-domain signal
  endfor
  Calculate the time-domain of signal
  Multiply the time-domain signal in amplifier gain for
  loss compensation
  Construct a white gaussian noise of proper variance as
  ASE noise and add it to the time-domain signal
  Calculate the frequency-domain of signal
endfor

## Slide 8: Receiver
DeMUX
Baseband Signal Recovery
Sampling and Symbol Detection
Matched Filtering
User 1
EDC
Comparing to TX Symbols
Baseband Signal Recovery
Sampling and Symbol Detection
Matched Filtering
User 2
Comparing to TX Symbols
Baseband Signal Recovery
Sampling and Symbol Detection
Matched Filtering
User N
Comparing to TX Symbols

## Slide 9: A Brief Introduction to EGN Model
An accurate, flexible and relatively fast model for non-linear interference
Based on perturbation approach and efficient in pseudo-linear regime of optical fiber
 | Accuracy | Flexibility | Limitation | Complexity
SSFM | Very High | Low | Almost Nothing! | High
EGN | Very Good to High | High | Pseudo-Linear Regime | Relatively-low
More on this later!

## Slide 10: Simulation Setup
Codes are written in Python.
A session for quick Python start-up is advantageous (but not mandatory!)
All the information you need, would be given to you in a PDF.

## Slide 11: Where You Come In …
The optical link part (and possibly the transmitter part) of the SSFM simulation is missing. Complete it and compare its results to those of the EGN model in given p2p scenarios.
The EGN model code given to you, is almost complete with a random bug (deliberately inserted!). Find the bug and fix it.
Hand in a complete report + correct codes. Codes must be able to be run standalone!

## Slide 12
Any Questions?

## Slide 13: Pseudo-Code for Link Transmission Simulation
 | for span in spans_of_link do: for fiber_section in span_fiber_sections do: Apply the half linear effects on frequency-domain signal Calculate the time-domain of signal Apply the non-linear span effects on time-domain signal Calculate the frequency-domain of signal Apply the half linear effects on frequency-domain signal endfor Calculate the time-domain of signal Multiply the time-domain signal in amplifier gain for loss compensation Construct a white gaussian noise of proper variance as ASE noise and add it to the time-domain signal Calculate the frequency-domain of signal Endfor